## Slide 1: Different “Flavors” of OFDM

## Slide 2
There are different “flavors” of OFDM according what we put in the Prefix:
data
P
data
P
data
P
time
Prefix
Three main choices:
CP-OFDM with Cyclic Prefix (CP)
ZP-OFDM with Zero Prefix (ZP)
TDS-OFDM (Time Domain Synchronous) with Pseudo-Random Prefix
Prefix
Prefix

## Slide 3
CP-OFDM with Cyclic Prefix
The most used: IEEE802.11, 802.16, Digital Video Broadcasting in Europe and many others
Advantages:
  Simple to implement
  CP good for synchronization (since it repeats)
Disadvantages:
  CP discarded (waste of transmitted power)
  possible nulls at subcarriers in fading channels
data
CP

## Slide 4
Reason for Null Carrier in CP
Let’s follow one subcarrier:
Steady state
CP
Transient
With CP, at the receiver we discard the transient and just look at steady state;
if the frequency response at the subcarriers frequency is zero (deep fading), then we completely loose that data of that subcarrier.
channel

## Slide 5
ZP-OFDM with Zero Prefix
Used in some standards (“WiMedia UWB” Personal Area Network for multimedia, short range, file transfer)
Advantages:
  in principle, there is never a null, if properly implemented
  no power loss in ZP
  suitable for Blind Equalization (see later)
Disadvantages:
  “proper implementation” cannot use FFT and is very inefficient
  keeps turning on and off: not good for components.
data
ZP
Reference: B. Muquet, Z. Wang, G.B. Giannakis, M. deCourville, P. Duhamel,” Cyclic Prefix or Zero Padding for Wireless Multicarrier Transmission?”, IEEE Transactions on Communications, Vol 50, no 12, December 2002

## Slide 6
Reason for Never a Null Carrier in ZP
Let’s follow one subcarrier corresponding to deep fading:
Steady state
ZP
Transients
No Inter Block Interference (IBI) due to the ZP
With ZP, you do not discard anything;
if the frequency response at the subcarriers frequency is zero (deep fading), then we still have a transient response, no matter what (most likely it will have low energy, but never zero)
channel

## Slide 7
Time Domain Synchronous TDS-OFDM with Pseudo-random Prefix (PP)
In Chinese Digital TV standard (DTMB)
Advantages:
  Excellent Synchronization
  Excellent channel estimation
Disadvantages:
  Slightly higher complexity (but worth it)
  Applicable to long OFDM frames (such as Digital Broadcasting)
data
PP
Reference: M. Liu, M. Crussiere, J.F. EHeard, “A Novel Data Aided Channel Estimation wit Reduced Complexity for TDS OFDM Systems,” to appear.

## Slide 8
OFDM-ZP and Channel Equalization
Channel Equalization in general (not OFDM yet).
1. Trained:
Channel
Equalizer
time
data
Training data
Training data
estimator
Receiver
It is based on training data, known at the receiver.

## Slide 9
2. Blind Equalization (general):
No training data
(something like “no hands!”)
Channel
Equalizer
estimator
Receiver

## Slide 10
How do we do Blind Equalization in general?
We need to exploit features of the signal. Mainly two approaches:
Constant Modulus (for BPSK and QPSK signals):
Channel
Equalizer
estimator
If QPSK or BPSK:
Determine which minimizes
Problem: non quadratic minimization and likely it converges to local minima

## Slide 11
Better Approach to general Blind Equalization:
Subspace method: the received signal is in a subspace determined by the channel.;
One approach: Fractionally Spaced Equalizers:
Transmitter,
Channel,
Receiver
symbol rate
M-QAM
DAC
Sample at twice the symbol rate
Same as:

## Slide 12
At the receiver, separate the two data streams (even and odd samples):
Transmitter,
Channel,
Receiver
M-QAM
DAC

## Slide 13
See a discrete time model
Take the Polyphase decomposition of the channel and ignore the noise (for simplicity):

## Slide 14
Apply Noble Identitites
=
=
=
“zero”
=
=
“zero”

## Slide 15
DAC+Transmitter+Channel+Receiver+ADC
They are the same!!! 

## Slide 16
Apply z-Transforms:
Multiply both:
Right Hand Sides are the same. Then :
Back in time domain:
This relates the channel parameters to the received data without knowledge of the transmitted message.

## Slide 17
Example. Take a first order case:
Polyphase decomposition:
Then:
In vector form:

## Slide 18
Compute Channel parameters from received signal:
Then the channel impulse response is proportional to the eigenvector corresponding to the smallest eigenvalue (zero if no noise) of
This means that the received signal ‘’lives” in a subspace.
The channel parameters “live” in the orthogonal subspace.
noise
Received signal
Channel parameters

## Slide 19
Mod and Demod with ZP OFDM
i-1
Take one OFDM Symbol (with index i ) :
Transmittedsignal
Channel
Received data
i
i+1
i-1
i
i+1

## Slide 20
Define the 2N points FFT, by zero padding
Due to the zero padding, convolution and circular convolution are the same:
Recall the transmitted data (drop the block index “i” for convenience:
Fact (easy to show):
Demodulation:

## Slide 21
N-IFFT
+ZP
P/S
TX
2N-FFT
S/P
RX
Choose even indices
ZP OFDM: one approach to Mod. and Demod.

## Slide 22
Blind Equalization with ZP OFDM
data
See the zero padded
Define:
Then: for all
Recall that DFT of the product is the circular convolution of the DFT’s:
where:

## Slide 23
Notice that for k even, non zero.
Then:
This relates even and odd frequency components:

## Slide 24
Since (neglect the noise and put back block index “i”):
This implies that, for each data block i for m=0,…,N-1
In matrix form, for the i-th received data block :

## Slide 25
In matrix form, for the i-th received data block :
Where we define:
a) the NxN diagonal matrices of even and odd 2N DFT components of the channel:
b) The Nx1 vectors of even and odd 2N DFT components of each received block:
c) The NxN matrix of this term defined earlier:

## Slide 26
This expression relates the received data blocks with the channel frequency response.
Now see how to actually compute the channel frequency response.
First collect a M received data blocks:
“Pack” all the se vectors in a matrix:

## Slide 27
Multiply both sides on the right by :
Multiply both sides on the right by :
Start with:
and you get:
This relates the channel freq. response H with the received signal Y.

## Slide 28
Summarize it so far:
1. Take M>N ofdm received frames :
2. For each frame, take the 2N point FFT by zero padding:
3. Separate even and odd subcarrier indices and “pack” them in two NxM matrices:

## Slide 29
Now we want to compute the channel from the expression
Define:
Since are diagonal matrices, here is how this expression looks like:

## Slide 30
Equate the m-th row on both sides (any one):
Just a scaling constant!
Demodulation:
For the i-th block. Take any arbitrary
Given just one known symbol you determine .

## Slide 31
Time Domain Synchronous TDS-OFDM with Pseudo-random Prefix (PP)
The PP facilitates synchronization and channel estimation
DFT Data Block
PP
Pseudo Noise
Pre- amble
Post- amble
The PP has its own Cyclic Prefix, both at the beginning (Pre-amble) and the end (Post-amble);
The Pseudo Noise (PN) changes for every frame.

## Slide 32
Application in Chinese Digital Terrestrial Television Broadcasting (DTTB).
In this standard the PN is an m-sequence of length N=255 BPSK symbols.
DFT Data Block
PP
3780
255
420
83
82
Post- amble: repeat first 82 PN samples
Pre- amble: repeat last 83 PN samples
A
B
C
C
A
In general (make the pre- and post- amble the same lengths for simplicity):

## Slide 33
A
B
C
C
A
*
=
Guard Interval
Channel
A
B
C
=
Fact:
Due to the repetitions, linear convolutions and circular convolutions of the Guard Interval are the same:

## Slide 34
A
B
C
C
A
*
=
A
B
C
=
Fact:
Now see the guard interval at the receiver and correlate with shifted PN:
A
DATA
C
B
Define:

## Slide 35
Then:
But:
Therefore:
and:

## Slide 36
Received data
DFT of DATA
DFT of DATA
GI
GI
Algorithm for Channel Estimation in TDS-OFDM: