## Slide 1
Channel Estimation from Data
Recall Impulse Response Identification from Correlation
Estimation of Time Spread and Doppler Shift
Simulink/Matlab Example
Stanford University Interim (SUI) Channel Models

## Slide 2
Estimation of Channel Characteristics from Input - Output data.
1. For Linear Time Invariant (LTI) systems:
Excite the system with white noise and unit variance
and compute the crosscorrelation between input and output

## Slide 3
In matlab:
1. Get data (same length for simplicity):
2. Compute crosscorrelation between input and output:
h=xcorr(x,y);
If x[n] is white noise, h[n] is the impulse response.

## Slide 4
2. For a Linear Time Varying Channel:
Goal: estimate time and frequency spread.
Known:
Sampling frequency
Upper bound on max Doppler Frequency
The impulse response changes with time

## Slide 5
1. Collect Data and partition in blocks of length :
X=reshape(x,N,length(x)/N);
Y=reshape(x,N,length(y)/N);
X,Y =
Within each block the channel is almost time invariant

## Slide 6
2. Estimate impulse response in each block :
h(:,i)=xcorr(Y(:,i),X(:,i))/N;
h =
h’ =
Each row is an impulse response taken at different times
Take the transpose:
plot((-N+1:N-1)/Fs, abs(h(:,i)));

## Slide 7
3. Compute Power Spectrum on each column of h’ (each row of h) , to determine time variability of the channel (If the channel is Time Invariant all columns of h are the same):
h’ =
H=fft(h’); S=H.*conj(H);
time
time
S =
time
Freq.

## Slide 8
4. Take the sum over rows for Doppler Spread and sum over columns for Time Spread (fftshift each vector to have “zero” term (sec or Hz) in the middle
St
Sf
Frequency Resolution:
Therefore if we want to a resolution in the doppler spread of (say) 1Hz, we need to collect at least 1 sec of data.
Time Resolution:

## Slide 9
Example:
% channel
Fs=10^6; % sampling freq. In Hz
P=[0,-2,-3]; % attenuations in dB
T=[0, 10, 15]*10^(-6); % time delays in sec
fd=70; %doppler shift in Hz
test_scattering.mdl

## Slide 10
Channel Output (Magnitude) with a QPSK Transmitted Signal:
t (sec)

## Slide 11
Time Spread
Frequency Spread
sum(S)/NB; sum of each column
sum(S’)/(2N-1); ave. of each row